1.Title
Operation Placement for
Application-Specific Digital Microfluidic Biochips
Mirela Alistar, Paul Pop, Jan Madsen
Technical University of Denmark, Lyngby
[Speaker Notes: My name is Mirela Alistar. from Denmark Tech Uni. Today I am going to present our work on the amazing domain of digital microfluidic biochips.]

---
2.Biochips
Biochips
Test tubes
Robotics
Microfluidics
Slide source: Krish Chakrabarty, Duke University
Automation
Integration
Miniaturization
Automation
Integration
Miniaturization
Automation
Integration
Miniaturization
[Speaker Notes: Biochips are designed to replace the traditional lab-equipment. There are different types of biochips, one that uses continuos flow, about which my colleague Morten will talk during the next presentation and the second type: the digital biochips that transport fluids as discrete amounts of nanoliter volumes, called droplets.]

---
Droplet-based Biochips
Biochip from Duke University
Digital Microfluidic Biochips (DMBs)
Input
port
Output
port
Sensor
[Speaker Notes: Here is a prototype from Duke Uni for such a droplet-based biochip. And this is how we represent one, as a 2d array electrodes. The electrodes are identical, so they can be used interchangeably, thus the electrode area is highly reconfigurable. There are also non-reconfigurable components on the biochip: - reservoirs preloaded with necessary fluids (samples, buffer, reagents) - sensors and detectors to measure the volume or the concentration of specific substances in the droplets]

---
Fluidic Operations
Video source: Advanced Liquid Logic http://www.liquid-logic.com/
[Speaker Notes: [To embed the ALL video] By moving the droplet from one electrode to another, all necessary operations to complete a biochemical protocol can be performed. This a demonstration video from ALL, a company that produces them. Initially the fluid is stored in a designated reservoir. A droplet is dispensed from the reservoir by activating a series or electrodes to form a finger and then splitting. Two droplets are mixed when they are brought together, merged and then transported for a period of time. Since all electrodes are identical, the mixing and splitting operations can be executed on any area on the biochip.]

---
Insert here a line about costs from ALL (producction plus reagents talk)
DMB Architecture
- General-Purpose Architecture
  - Reconfigurable
  - Versatile
  - Fault-tolerant
- Application-Specific Architecture
  - Designed for one application
  - Reduced costs
    - Production costs
    - Reagent costs
Input
port
Output
port
Sensor
Buffers
Reagents
In R1
Samples
Waste
Detectors
In S1
In S2
In S3
In R2
In B1
In B2
[Speaker Notes: We distinguish between 2 types of architecture: a general purpose one and an application specific one. The general purpose architecture has the shape of a rectangle of electrodes. It is easy to reconfigure and can be used for multiple biochemical protocols. Also, it is fault-tolerant, as the defective electrodes can be easily replaced by the functional ones. An application specific architecture is specially designed for a specific biochemical protocol. The shape is irregular with no redundant electrodes, only the necessary ones are kept. The reservoirs are designed to optimize the use of necessary fluids. Its big advantage comes from cost reduction. Not only the surface area is optimized for that specific architecture, reducing the production costs, but also the reservoirs which lead to lowering reagents costs.]

---
Application-Specific Biochips
Biochip for Newborn Screening
http://www.liquid-logic.com/
Biochip for Sample Preparation
http://www.nugeninc.com/
[Speaker Notes: These are 2 examples of such application-specific architectures from ALL: One used in clinical trial when newborn babies are screened for severe genetical diseases and another one used for sample preparation. On these architectures we can see the reservoirs, here are the detectors, and these are the electrodes from droplet transportation and mixing.]

---
Architecture Selection
- Reduced cost architectures
- Fault-tolerant architectures
- Increase the yield of DMBs
Insulator degradation
Bioassay
Architecture
Selection Tool
[ASPDAC, 2013]
Module Library
Component Library
Architecture
Max No. of faults
Application-Specific Fault-Tolerant Architecture Synthesis for DMBs, M. Alistar, P. Pop, J. Madsen
[Speaker Notes: We have been looking recently into what we call the architecture selection problem, which means designing automatically, for a given bioassay, an application specific architecture of minimal costs that can also be fault-tolerant. Fault-tolerance increases the yield, which together with cost reductions, are essential for market success of DMBs. We have just published our proposed AS tool, that takes as input .. and outputs an app-spec arch.]

---
Biochemical Application Model
[Speaker Notes: We represent a biochemical protocol, or an application as we call it, as an graph. The nodes represent the fluidic operations of the applications, and the edges represent the dependencies between them. For example, the directed edge between mix O18 and operation O21 signifies that operation O18 has to finish before O21 can begin. Also, O21 uses as input the droplet outputed by O18.]

---
 Synthesis Flow
Biochemical Application
Synthesis
Application
Execution
Electrode actuation sequence
Fluidic Operations Library
Deadline requirement
Biochip
Computer
[Speaker Notes: We get from an application modeled as a graph to moving droplets on the biochip, through synthesis. Synthesis is the process that takes as input … and outputs the … which means the order in which the electrodes will be activated so that the necessary fluidic operations will perform.]

---
4. Synthesis tasks
Synthesis: Main steps
Allocation
Binding
Operation	Area (cells)	Time (s)
Mix	2 x 4	3
Mix	2 x 2	4
Dilution	2 x 4	4
Placement
Scheduling
0
3
6
8
O5
O6
M1
O7
M2
Mix O5
O2
O1
O4
O3
O5
O7
O6
source
sink
[Speaker Notes: Synthesis is performed on a computer and it consists of 4 main steps: ….]

---
Synthesis: Main steps
Allocation
Binding
Operation	Area (cells)	Time (s)
Mix	2 x 4	3
Mix	2 x 2	4
Dilution	2 x 4	4
Placement
Scheduling
0
3
6
8
O5
O6
M1
O7
M2
Mix O5
O2
O1
O4
O3
O5
O7
O6
source
sink
[Speaker Notes: In this work we are interested in the placement step, that finds the location on the biochip for each operation.]

---
Circular-route module
[Speaker Notes: We propose a placement strategy based on circular-route modules, which are are circular routes of any shape, including rectangular, on which droplets move until the operation is completed. The electrodes assigned for one module are not considered occupied and can be used for other operations. As a consequence, the routes for different operations may overlap over several electrodes. In order to avoid undesired droplet merging for intersecting routes during runtime, we instruct one of the droplets to take a detour from its predetermined route as shown in the Figure. .. or to wait until the droplet passed by. In order to avoid contamination, we minimize the number of overlapping electrodes among the circular-route modules used by operations that have contamination conflicts. By doing that, we restrict the washing operations to the overlapping electrodes, thus minimizing the execution overhead due to contamination avoidance.]

---
Circular-route module
[Speaker Notes: We propose a placement strategy based on circular-route modules, which are are circular routes of any shape, including rectangular, on which droplets move until the operation is completed. The electrodes assigned for one module are not considered occupied and can be used for other operations. As a consequence, the routes for different operations may overlap over several electrodes. In order to avoid undesired droplet merging for intersecting routes during runtime, we instruct one of the droplets to take a detour from its predetermined route as shown in the Figure. .. or to wait until the droplet passed by. In order to avoid contamination, we minimize the number of overlapping electrodes among the circular-route modules used by operations that have contamination conflicts. By doing that, we restrict the washing operations to the overlapping electrodes, thus minimizing the execution overhead due to contamination avoidance. Example of how we calculate the completion time for a CRM.]

---
Problem
- Given
  - Biochemical application
  - Application-specific architecture
- Determine
  - An circular-route placement of operations, so that the
    application completion time is minimized
[Speaker Notes: Which brings us to our problem: placement of operations on a DMB, formulated as follows: For a given biochemical protocol/application, that has to executed on a also given application-specific architecture, we have to determine for each operations the corresponding circular-route modules so that the application completion time is minimized.]

---
CRM Library
Example of library for circular-route modules
Operation	Circular-route module	Operation time (s)
Mix	CRM1	3.05
Mix	CRM2	2.28
Mix	CRM3	2.18
[Speaker Notes: This is an example of library for CRM. For this app-specific biochip we have obtained this library of CRM, where module 1 completes in .. secs .. etc]

---
Building a CRM library
- Identify restricted rectangles (RRs)
- Use RRs as guidelines for obtaining CRMs
- CRMs are determined so that they
  minimize operation completion time
- CRMs are stored in a library
Determining circular-route modules

---
Synthesis
Allocation
Binding
Operation	Circular-route module	Operation time (s)
Mix	CRM1	3.05
Mix	CRM2	2.28
Mix	CRM3	2.18
Placement
Scheduling
[Speaker Notes: Our placement strategy can be integrated with any synthesis approach. As we can see here, all we have to do is to plug in our CRM library and our placement strategy.]

---
Placement of CRMs
- Integrated with any available synthesis
- List Scheduling – based synthesis
- Select a CRM from library for each operation
  - such that the completion time is minimized
- Place the CRM on the biochip
- Schedule the operation
[Speaker Notes: For example, integrating our placement with LS based synthesis is done by - selecting a CRM from the library for each operation - such that the completion time is minimized - placing the CRM on the biochip - and scheduling the operation]

---
Experiments: setup
- Biochemical applications:
  - In-vitro diagnosis on human physiological fluids (IVD)
  - 3 synthetic benchmarks (SB1 - SB3)
- Architecture:
  - IVD – obtained with our Architecture Synthesis Tool
- Implementation:
  - Java
- Evaluation:
  - Efficiency in terms of application completion time
  - Comparison with Routing-based synthesis
[Speaker Notes: From the paper … to be completed]

---
Experimental results
App. (ops*)	Arch.	MinR, MaxR	δR (s)	δCRM (s)	Deviation (%)
IVD (23)	45 / ( 2, 2, 2 )	[ 3, 5 ]	18.4	11.73	36
SB1 (50)	96 / ( 1, 2, 1 )	[ 3, 5 ]	29.39	23.9	18.6
SB2 (70)	103 / ( 2, 2, 2 )	[ 3, 6 ]	31.03	20.15	35
SB3 (90)	125 / ( 2, 2, 2 )	[ 3, 8 ]	42.51	27.87	34
G
G
* We ignored the detection operations for experiments
IVD – in-vitro diagnosis, SB – synthetic benchmark
δ - application completion time
G
[Speaker Notes: From the paper …]

---
Conclusions
- Selection of architectures that minimize application completion time
- Strategy for placement of operations
  - We built a CRM-library
  - Better use of area
  - Better operation completion times
- Integration with our Architecture Selection tool
[Speaker Notes: We conclude by saying that under the bigger problem of architecture selection, we proposed a strategy for placement of operations for application-specific architectures, that uses better the available area, resulting in better app completion times. For further work we are looking into integrating our placement strategy wit out arch selection tool.]

---
Backup slides

---
List Scheduling

---
Routing-based Operation Execution
90o
0o
0o
90o
90o
90o
90o
0o
0o
90o
Operation	Area (cells)	Time (s)
Mix	2 x 2	10
Mix	2 x 3	6
Mix	1 x 4	5
p90 = 0.1%
p0 = 0.29% p00 = 0.58%
p180 = -0.5%
E. Maftei, P. Pop, J. Madsen, “Routing-based synthesis of digital microfluidic biochips”, 2012
0o
0o
180o
0o
0o
180o

---
Droplet vs. Module Compilation
Droplet based
- routing base operation execution
- the position of the droplet is tracked
- better use of space
Module based
- module library
- black boxes
- protection borders
Operation	Area (cells)	Time (s)
Mix	2 x 4	3
Mix	2 x 2	4
Dilution	2 x 4	4
0o
180o
180o
0o
0o
0o
0o
0o
90o
0o
90o
0o
0o

---
Placement
Routing-based
Module-based
Module-based
Module-based
Droplet-aware
Segregation border
2x4 Mixer
2x4 Mixer
Deviated route
2x4 Mixer
Deviated route
[Speaker Notes: Our current work tackles the Placement task, which means deciding the operations position on the biochip. In past research, several Placement strategies have been proposed.]

---
Module-based
Dis B
Dis S
Dis R
Segregation border
2x4 Mixer
Dispensing
Reservoirs
Routing –	a post-synthesis step
[Speaker Notes: The first one was a module-based Placement, a strategy which groups the electrodes into rectangles, called modules, on which the operations execute. These modules are like black boxes: the droplets are transported to them and left there to execute the operation, with no track of their behaviour inside the module. Once a droplets enters a module, the corresponding electrodes are considered occupied and cannot be used for other operations until the current one is finished. Moreover, the droplets need at least one electrode distance between them, otherwise they will merge instantly. So, the modules need a segregation border around them to avoid accidental merging of droplets. It is easy to notice that a lot of biochip area is wasted for the segregation borders.]

---
Droplet-aware
Dis B
Dis S
Dis R
2x4 Mixer
Droplet position is known
No segregation borders
Better use of area
Droplets stopped or deviated
to avoid accidental merging
Integrated routing
Deviated route
[Speaker Notes: In order to better use the biochip area, droplet-aware placement keeps track of the droplet position inside the modules. By doing that, the segregation border is not needed anymore, as the droplets can be either stopped or deviated when in danger of accidental merging. As observed in the figure, in order to avoid merging with the green droplet, the red droplet is deviated to this new route.]

---
Routing-based
Dis B
Dis S
Dis R
2x4 Mixer
No modules
Contamination issues
Deviated route
[Speaker Notes: The routing-based placement eliminates completely the modules, allowing the droplets to freely move all over the biochip area, until the operation is completed. The main concern when using routing-based placement is contamination, in which case, long routes that traverse that whole biochip might need washing, instead of a restricted rectangular area.]

---
Mixers
flow reversibility issue
one pivot issue
Mixing is faster if:
No 180o moves
Multiple pivots
No change of direction
 1x4 module, t = 4.6 s
90o
90o
90o
90o
 2x2 module, t = 9.95 s
 2x3 module, t = 6.1 s
Routing-based operation execution
 2x4 module, t = 2.9 s
0o
180o
180o
0o
0o
0o
[Speaker Notes: When using routing-based placement, the droplets move freely until the operation is completed. But we need to know when the operation is completed, in order to stop the droplet movement. For that, we use the routing based operation execution model, which decomposes the operation into basic moves and calculates the impact of each basic move on the operation completion time. For example, the mixing on a 1x4 module consists of 3 moves: 2 of 0 degrees and one of 180 degrees. Researchers performed experiments to study the mixing operation. When using a 1x4 mixer, researchers observed that turning back the droplets with a 180 degree move, reverses partially the mixing operations, due to flow reversibility. Next, they tried a 2x2 mixer, and obtained a worse mixing time due to the fact that the droplets were pivoting around one point only. For a 2x3 mixer they obtained better mixing time, as the droplets had 2 pivots. The best time was obtained for a 2x4 mixer, because keeping the droplets movement in one direction helps the mixing. Using these observations and the experimentally obtained completion times, RBOE model estimates, for each move, the percentage completion towards operation execution. -]

---
Optimization: Simulated Annealing
A0 - initial architecture
T0 - initial temperature
TL – temperature length
eps – cooling rate
temp = T0;
A = A0;
repeat
while (temp < TL) do
Anew = moves(A); //generate new architecture
delta = Objective(A) – Objective(Abest);
if (delta<0)
Abest = Anew;
elseif (Math.random < e-delta/temp) //accept bad solutions with low probability
Abest = Anew;
endif
endwhile
temp = temp * eps;
until stop criterion is true
[Speaker Notes: So our focus is to determine if application-specific architectures are more cost-effective than the general-purpose ones. In order to do that we use a known metaheuristic called Simulated Annealing to optimize solution space exploration. SA explores the solution space using design transformation called moves. It starts with an initial solution, which is altered by these moves into a new solution. Each new solution obtained by using the moves is evaluated by an objective function. Our objective function has two members: - the production cost of the new architecture (which is the cost of physical components) - a penalty cost in case the architecture does not meet the deadline constraint A new solution, obtained by using the SA moves, is accepted if it is an improved one, i.e. is has a lower cost than the best-so-far solution. However, SA also accepts worse solutions, with a probability that depends on the objective function and a control parameter called temperature. SA is controlled by a cooling schedule that has specific parameters: - Initial temperature TI - temperature length - a cooling ratio epsilon The cooling schedule is calibrated for each protocol. Note: we calibrate like that: we use large parameters that would allow SA to run for a very long time … etc Note: some stuff on SA]

---
Synthesis
[Speaker Notes: And here, how much I say?]

---
Libraries
Component Library
Virtual Devices Library

---
Build a CRM library