Compilation and Synthesis for Fault-Tolerant Digital Microfluidic Biochips
Compilation and Synthesis for Fault-Tolerant
Digital Microfluidic Biochips (DMBs)
Mirela Alistar, advisors: Paul Pop, Jan Madsen
Biochemical Application Model
Biochip Architecture Model
Challenge: Faults
Runtime Compilation for Error Recovery
Recovery Techniques
Compilation Tasks
Application Specific Architecture
Problem Formulation Cost Evaluation
Fault-Tolerant Operation Execution
Architecture Synthesis
A biochemical application is modeled as a directed graph, where the nodes represent the operations and the edges represent the dependencies between them. Examples of operations are: dispensing, mix, dilution, optical detection, merge. Droplets are transmitted through the edges from one operation to its successor operation. An operation is ready to execute when its inputs have arrived.
DMB for Newborn Screening
(Advanced Liquid Logics, Inc.)
Application-specific biochip model
DMB for Sample Preparation
(Nugen, Inc.)
Given
A biochemical application
A library of components
The number k of permanent faults
Determine an application-specific architecture so that
the cost is minimized and
the application completes within deadline
for any occurrence of the k permanent faults
Cost_{A} = sum {N_{M_i} times Cost_{M_i}} + sum {N_{R_i} times Cost_{R_i}}
A biochip architecture is modeled as an array of electrodes. The biochip contains devices such as dispensing and waste reservoirs and sensors. Sensors can be used to determine the result of the bioassay or for error detection.
Operations execute within specified areas called modules, which can be placed on any electrodes of the biochip. A mixing operation is executed when two droplets are moved to the same location and then transported together according to a specific pattern. A split operation is done by keeping the electrode on which the droplet is resting turned off, while applying concurrently the same voltage on two opposite neighboring electrodes. Dilution is a mixing followed by a split.
These architectures are general-purpose and highly reconfigurable.
Component cost
Fluidic cost
Space redundancy creates redundant droplets before the error was detected.
Time redundancy re-executes the erroneous operations after the error was detected.
 Removing electrodes
 Reconstructed route
During the execution of the application, the volume of droplets can vary erroneously due to transient faults. The errors propagate throughout the entire application, affecting eventually the result of the bioassay. Biochemical applications have sensitivity to faults during runtime, such as an unbalanced split.
Permanent faults, introduced during fabrication, can prevent the execution of the application.
Hence, there is an imperative need for design methodologies for fault-tolerant DMBs.
Adjusted route
Adding electrodes
Unbalanced split
Insulator degradation
Dielectric breakdown
Mirela Alistar mali@dtu.dk Advisors: Paul Pop, Jan Madsen
Embedded Systems Engineering Section, DTU Compute
Technical University of Denmark
Waste
Dis S
Dis B
Dis B
Dis R
Dis R
Sensor
Segregation border
2x5 Module
Dispensing
Reservoirs
Storage
1. Initial offline
redundancy assignment
2. Offline compilation
Offline
Detection
feedback
5. Online compilation
4. Redundancy optimization
strategy
3. Recovery
Online
Biochip
Sensor
Electrode
actuation
sequence
Buffers
Reagents
In R1
Samples
Waste
Detectors
In S1
In S2
In S3
In R2
In B1
In B2
O8
Dilution
Mix
Mix
O11
O10
In R
O9
In B
O7
O12
In S
O2
O1
O3
Mix
In S
In R
O6
O5
O4
O13
O14
O15
Dilution
Dilution
Dilution
In R
In R
In B
Waste
In B
In R
In S
Scheduling
Binding
Allocation
Operation	Area	Time
Mix	2x5	2
Mix	2x4	3
Mix	2x2	10
Detection	1x1	30
0
2
4
6
8
10
12
14
16
18
20
22
24
26
O3
O1
O10
O14
O9
O2
O12
O7
O4
O11
O15
O13
O5
O6
O8
S4
In S
In B
In R
M1
M2
Storage1
Deadline
Storage2
Storage3
S10
S13
Waste
In B
In R
Storage2
In S
M1
M2
M4
M3
Storage1
Storage3
Placement
Routing
Error
Recovery
O5
O6
R5
O7
O5
Error
Recovery
O6
O7
R5
X
X
X
X
Detector
In S
In B
In R
O8
Dilution
Mix
Mix
O11
O10
In R
O9
In B
O7
O12
In S
O2
O1
O3
Mix
In S
In R
O6
O5
O4
O13
O14
O15
Dilution
Dilution
Dilution
In R
In R
In B