Scheduling and Voltage Scaling for Energy/Reliability Trade-offs in Fault-Tolerant Time-Triggered Embedded Systems
Kåre Harbo Poulsen
August 23, 2007

---
Outline
Introduction
Motivation
Problem Formulation
Implementation
Experiments and Results
Conclusions
Q&A

---
Embedded Systems
[Speaker Notes: Embedded systems are small computer systems that are build into applications to do special purpose tasks. Use the example to illustrate the different constraints. “Presents an interesting optimisation problem, if all these constraints are to be met simultaneously” real-time -> good scheduling algorithms (meet deadlines) Reliable -> fault-tolerance Low power -> energy management “In my thesis I have developed a tool for doing this efficiently.”]

---
Embedded Systems
Embedded MP-SoCs
  - Single purpose
  - Real-time
  - Reliable
  - Low power
[Speaker Notes: Embedded systems are small computer systems that are build into applications to do special purpose tasks. Use the example to illustrate the different constraints. “Presents an interesting optimisation problem, if all these constraints are to be met simultaneously” real-time -> good scheduling algorithms (meet deadlines) Reliable -> fault-tolerance Low power -> energy management “In my thesis I have developed a tool for doing this efficiently.”]

---
Design of Embedded Systems

---
Summary
Design tool for Embedded MP-SoCs
  - Schedule and Mapping
  - Ti	ming constraints
  - Fault tolerant / reliable
  - Energy efficient

---
Embedded Systems Model
Input
  - Application
  - Architecture
Output
  - Mapping
  - Schedule
P1
m1
P2
P3
m2
P4
P5
PE
PE
1
2
P
4
4
P
4
4
P
3
3
3
P
4
4
4
P
4
4
5
PE1
PE2
Bus
Deadline

---
Faults
Permanent faults are decreasing
Transient faults are increasing
From: Cristian Continescu, Trends and challenges in VLSI circuit reliability, 2003

---
Fault-Tolerance
Tolerate faults gracefully
Expressions for reliability for fault-tolerance
Re-execution
Passive Replication
Replication
[Speaker Notes: Hardware faults are not common anymore]

---
Reliability
Single execution:
R_{single} = e^{−λc} = 1 − ρ
Fault-tolerance:
R_{FT} = 1- prod from{i=1} to{k} (1-R_i)
Application
R_{App} = prod from {P_i in A} R_{P_i}
P1/2
P4/5

---
Embedded Systems Model
Input
  - Application
  - Architecture
  - Reliability goal: 0.999 999 999
m1
m2
PE
PE
Reliability goal missed
P
4
4
P
4
4
P
3
3
3
R0=0.999 981
P
4
4
4
P
4
4
5

---
Fault-Tolerant Scheduling
Input
  - Application
  - Architecture
  - Reliability goal: 0.999 999 999
Fault-tolerance for k=1 faults
m1
m2
PE
PE
Reliability goal met
P
4
4
P
4
4
P
3
3
3
R0=0.999 999 999 927
P
4
4
4
P
4
4
5
k=1

---
Fault-Tolerant Scheduling
Fault tolerant scheduler
  - Full transparency
    - Good debugability
    - Little memory
m1
m2
PE
PE
P
4
4
P
4
4
P
3
3
3
Fully Transparent Scheduling
P
4
4
4
P
4
4
5
k=1
Only 1 fault

---
Fault-Tolerant Scheduling
Can be done faster
  - Sacrifice local transparency
m1
m2
PE
PE
P
4
4
P
4
4
P
3
3
3
Fully Transparent Scheduling
P
4
4
4
P
4
4
5
k=1
Only 1 fault

---
Fault-Tolerant Scheduling
Can be done faster
  - Sacrifice local transparency
  - More complex online scheduler
m1
m2
PE
PE
P
4
4
P
4
4
P
3
3
3
Slack Sharing Scheduling
P
4
4
4
P
4
4
5
k=1
P1/2
P4/5
Only 1 fault

---
Fault-Tolerant Scheduling
Even faster
  - Sacrifice all transparency
  - Schedule for each fault scenario
m1
m2
PE
PE
P
4
4
P
4
4
P
3
3
3
Slack Sharing Scheduling
P
4
4
4
P
4
4
5
k=1
P1/2
P4/5

---
Fault-Tolerant Scheduling
Even faster
  - Sacrifice all transparency
  - Schedule for each fault scenario
  - At most k re-executions
m1
m2
PE
PE
P
4
4
P
4
4
P
3
3
3
P
4
4
4
P
4
4
5
k=1

---
Fault-Tolerant Scheduling
Even faster
  - Sacrifice all transparency
  - Schedule for each fault scenario
  - At most k re-executions
m1
m2
PE
PE
P
4
4
P
4
4
P
3
3
3
P
4
4
4
P
4
4
5
k=1

---
Fault-Tolerant Scheduling
Even faster
  - Sacrifice all transparency
  - Schedule for each fault scenario
  - At most k re-executions
  - All faults information is shared
m1
m2
PE
PE
P
4
4
P
4
4
P
3
3
3
Conditional Scheduling
P
4
4
4
P
4
4
5
k=1

---
Fault-Tolerant Schedulings
Fully Transparent Scheduling
m1
m2
Slack Sharing Scheduling
PE
PE
P
4
4
P
4
4
P
3
3
3
P
4
4
4
P
4
4
5
Conditional Scheduling
k=1
P1/2
P4/5

---
Energy Management
Goal: minimise energy consumption
  - Dynamic voltage scaling
100% Vss
100% E0
100% E0
66% Vss
44% E0
33% Vss
11% E0

---
Energy Management
Fully Transparent Scheduling
m1
100% E0
m2
Slack Sharing Scheduling
PE
PE
P
4
4
P
4
4
P
3
3
3
P
4
4
4
P
4
4
5
Conditional Scheduling
k=1
P1/2
P4/5

---
Energy Management
Fully Transparent Scheduling
m1
100% E0
m2
Slack Sharing Scheduling
PE
PE
P
4
4
P
4
4
P
3
3
63% E0
3
P
4
4
4
P
4
4
5
Conditional Scheduling
k=1
P4/5

---
Energy Management
Fully Transparent Scheduling
m1
100% E0
m2
Slack Sharing Scheduling
PE
PE
P
4
4
P
4
4
P
3
3
63% E0
3
P
4
4
4
P
4
4
5
Conditional Scheduling
38% E0
k=1
P4/5

---
Energy Management
Fully Transparent Scheduling
m1
100% E0
m2
Slack Sharing Scheduling
PE
PE
P
4
4
P
4
4
P
3
3
63% E0
3
P
4
4
4
P
4
4
5
Conditional Scheduling
38% E0
k=1
P4/5

---
Reliability Model
Linear model (Fixed voltage)
  - Frequency is scaled
  - Linear relation between fault probability and frequency (due to longer execution time)
Exponential model
  - Frequency and voltage is scaled equally
  - Lower voltages leads to smaller critical energy
  - Fault rate at minimum frequency
λ_0 cdot 10^d, ~ d>0
Dakai Zhu,the Effects of Energy Management on Reliability in RT Embedded Systems, 2004

---
Reliability and Energy
Lowering voltage increases no. faults
  - Lower energy particles cause fault
λ(f) = λ_0 10 ^{{d(1-f)} over {1-f_{min}} }
Dakai Zhu, Reliability-Aware Dynamic Energy Management in
Dependable Embedded Real-Time Systems, 2006

---
Energy Management
Fully Transparent Scheduling
m1
R=0.999 999 999 93
100% E0
m2
Slack Sharing Scheduling
PE
PE
R=0.999 999 999 25
P
4
4
P
4
4
P
3
3
63% E0
3
P
4
4
4
Reliability goal missed
P
4
4
5
Conditional Scheduling
R=0.999 999 958 208
38% E0
k=1
P4/5

---
Outline
Introduction
Motivation
Problem Formulation
Implementation
Experiments and Results
Conclusions
Q&A

---
Energy/Reliability Trade-off
Reliability goal: 0.999 999 9
R=0.999 999 987
100% E0
P6
N2
N2
N2
100%
100%
100%
66%
66%
66%
33%
33%
33%
k = 1
k = 1
k = 1
Rg=0.999 999 900
Rg=0.999 999 900
Rg=0.999 999 900

---
Energy/Reliability Trade-off
Reliability goal: 0.999 999 9
Set reliability as hard constraint
Reliability goal missed
R=0.999 999 878
68% E0
P6

---
Energy/Reliability Trade-off
Reliability goal: 0.999 999 9
Set reliability as hard constraint
Trade-off 5% energy
Meets reliability goal
Reliability goal met
R=0.999 999 920
P6
73% E0

---
Outline
Introduction
Motivation
Problem Formulation
Implementation
Experiments and Results
Conclusions
Q&A

---
Problem Formulation
Input
  - Application
  - Architecture
  - Reliability goal
Decide
  - Fault-Tolerant Scheduling
  - Mapping
  - Fault-Tolerance Policy
While optimising for
  - Energy
  - Under hard reliability goal

---
Implementation
Problem is NP-Complete
  - Normally solved using “best effort” heuristics
Use constraint logic programming
  - Good performance with NP-completeness
  - Optimal solutions are feasible
  - Flexible model
  - ECLiPSe-CLP

---
Constraints for Embedded Systems
Precedence constraint
m1
Start(P_j) >= forall _{e_{ij}} Start(P_i) + Duration(P_i)
m2
PE
PE
P
4
4
P
4
4
P
3
3
3
P
4
4
4
P
4
4
5

---
Constraints for Embedded Systems
Precedence constraint
m1
Start(P_j) >= forall _{e_{ij}} Start(P_i) + Duration(P_i)
m2
PE
PE
P
4
4
P
4
4
P
3
3
3
P
4
4
4
P
4
4
5

---
Constraints for Embedded Systems
Precedence constraint
Resource constraint
m1
m2
Mapping(P_i) <> Mapping(P_j) newline v Start(P_i) >= Start(P_j) + Duration(P_j) newline v Start(P_j) >= Start(P_i) + Duration(P_i)
PE
PE
P
4
4
P
4
4
P
3
3
3
P
4
4
4
P
4
4
5

---
Constraints for Embedded Systems
Precedence constraint
Resource constraint
Timing constraint
m1
m2
Start(P_i) + Duration(P_i) <= Deadline
PE
PE
P
4
4
P
4
4
P
3
3
3
P
4
4
4
P
4
4
5

---
Fault-Tolerance Constraints
Changed precedence constraint
m1
Start(P_j) >= forall _{e_{ij}} Start(P_i) + Duration(P_i)(k+1)
m2
PE
PE
P
4
4
P
4
4
P
3
3
3
P
4
4
Fully Transparent Scheduler
4
P
4
4
5
k=1

---
Fault-Tolerance Constraints
More complex to model
  - Create separate schedule for recoveries
m1
m2
Mapping(P_i) = Mapping(P_j) newline v Start(P_j) >= Endtime(S_i) newline
PE
PE
P
4
4
P
4
4
P
3
3
3
Slack Sharing Scheduler
P
4
4
4
P
4
4
5
k=1
P1/2
P4/5

---
Fault-Tolerance Constraints
Schedule for all fault scenarios
  - These are captured by an FT-CPG
m1
m2
PE
PE
P
4
4
P
4
4
P
3
3
3
Conditional Scheduler
P
4
4
4
P
4
4
5
k=1

---
Fault-Tolerance Constraints
m1
m2
PE
PE
P
4
4
P
4
4
P
3
3
3
Conditional Scheduler
P
4
4
4
P
4
4
5
k=1
P1,1
P1,2
P2,2
P3,2
P4,2
P2,1
P3,1
P4,1
P2,3
P3,3
P4,3
P4,5
P4,4
FP1
FP2
FP3
FP4
P5,2
P5,3
P5,4
P5,6
P5,1
P5,7
FP5

---
Fault-Tolerance Constraints
m1
m2
PE
PE
P
4
4
P
4
4
P
3
3
3
Conditional Scheduler
P
4
4
4
P
4
4
5
k=1
P1,1
P1,2
P2,2
P3,2
P4,2
P2,1
P3,1
P4,1
P2,3
P3,3
P4,3
P4,5
P4,4
FP1
FP2
FP3
FP4
P5,2
P5,3
P5,4
P5,6
P5,1
P5,7
FP5

---
Fault-Tolerance Constraints
m1
m2
PE
PE
P
4
4
P
4
4
P
3
3
3
Conditional Scheduler
P
4
4
4
P
4
4
5
k=1
P1,1
P1,2
P2,2
P3,2
P4,2
P2,1
P3,1
P4,1
P2,3
P3,3
P4,3
P4,5
P4,4
FP1
FP2
FP3
FP4
P5,2
P5,3
P5,4
P5,6
P5,1
P5,7
FP5

---
Fault-Tolerance Constraints
Schedule for all fault scenarios
  - These are captured by an FT-CPG
m1
m2
MutuallyExclusive(P_i, P_j) newline v ResourceConstraint
PE
PE
P
4
4
P
4
4
P
3
3
3
Conditional Scheduler
P
4
4
4
P
4
4
5
k=1

---
Outline
Introduction
Motivation
Problem Formulation
Implementation
Experiments and Results
Conclusions
Q&A

---
Comparison of Schedulers

---
Comparison of Schedulers

---
Reliability and Energy Trade-offs

---
Outline
Introduction
Motivation
Problem Formulation
Implementation
Experiments and Results
Conclusions
Q&A

---
Conclusions
Design tool for doing
  - Fault tolerant scheduling
  - Mapping
  - Policy assignment
Optimising for
  - Minimal energy
  - Hard constraints for timing and reliability
Message:
  - Reliability can be met at little energy cost

---
Contributions
Design optimisation for energy minimisation under reliability and timing constraints
  - “Design Optimistaion of Low-Power Reliable Real-Time Embedded Systems” RTSS (in preparation)
Optimisation method that decides the voltage scaling
  - “Scheduling and Voltage Scaling for Energy/Reliability Trade-offs in Fault-Tolerant Time-Triggered Embedded Systems” CODES+ISSS (submitted)
Efficient constraint logic programming-based scheduling technique
  - “A Constraint Logic Programmnig Framework for the Synthesis of Fault-Tolerant Schedules for Distributed Embedded Systems” ETFA (submitted)

---
Present Work
Credit search based heuristic
Addition of messages
  - TDMA FT scheduling
Heterogeneous architectures
  - Both in terms of speed and reliability

---
Questions and Answers
[Speaker Notes: Embedded systems are small computer systems that are build into applications to do special purpose tasks. Use the example to illustrate the different constraints. “Presents an interesting optimisation problem, if all these constraints are to be met simultaneously” real-time -> good scheduling algorithms (meet deadlines) Reliable -> fault-tolerance Low power -> energy management “In my thesis I have developed a tool for doing this efficiently.”]

---
Reliability
Single execution:
R_{single} = e^{−λc} = 1 − ρ
Fault-tolerance:
R_{FT} = 1- prod from{i=1} to{k} (1-R_i)
Application
R_{App} = prod from {P_i in A} R_{P_i}
P1/2
P4/5